| re: Dell 1025HE No score for this post | April 2 2003, 2:19 PM |
| --- | --- |

Unfortunatley these adjustments are done electronically. In some Nokia monitors you have to solder a wire link to enable factory alignment mode; adjustments are then done by the OSD. Some more recent models have a service mode which is entered by holding down the enter button whilst powering on the monitor. The OSD will ask for a password, enter 7711 using the + and - keys and press enter and it will display the service menu. I don't have a service manual for your particular chassis but you could try the second method to see if that works first.

| Nokia service mode No score for this post | April 3 2003, 4:18 AM |
| --- | --- |

Hi you can enter the service mode on the type you have to connect the wire link to but without this link the values are not saved. I use a small crocodile clip as the link is made top to bottom on a pcb edge connector. Rich

I can acess a service mode, where I can adjust VG2, RGB Gain & Black Level Cutoff folling this procedure:

1.) Turn Monitor off
2.) Push Menu Button for 4s during switch on of the Monitor, release and push Menu Button again.
3.) Now I have to enter service password wich is 7711 !!
4.) All adjustments, VG2, RGB Gain & Black Level Cutoff can be done using menu.